## Slide 1
Design and Analysis of a Planar Compliant Mechanism
ME 7751 Project 2 presentation
Ava Merrifield, The Ohio State University
Spring 2026

## Slide 2
Motivation and Objectives
Compliant mechanisms enable motion through elastic deformation.
Goal: connect PRB analytical modeling, FEA validation, and an interactive app.
Focus on a planar side-crank compliant slider mechanism.

## Slide 3
Mechanism Description
Rigid crank drives a flexible coupler to displace a grounded slider.
Planar compliant linkage with large deflections in the coupler.
Relevant for positioning, amplification, and compliant actuation.

## Slide 4
Problem Definition
Develop an analytical PRB model for the mechanism.
Validate the model using Abaqus-based FEA.
Compare torque and slider displacement predictions.

## Slide 5
Analytical Modeling Methodology
Use Pseudo-Rigid-Body (PRB) reduced-order modeling.
Derive the analytical model for the compliant coupler.
Document assumptions, governing equations, and derived metrics.

## Slide 6
Howell-Midha PRB Derivation
Based on classical fixed-pinned beam parametric deflection.
Uses characteristic length ratio λ = 2K_b/π ≈ 0.541.
Equivalent torsional stiffness coefficient K_b' = 12.7.

## Slide 7
My PRB Model Derivation
Uses a fitted tip path with radius factor γ = 0.8517.
Includes a characteristic pivot at the crank-coupler joint.
Defines torque via an equivalent spring at the pivot.

## Slide 8
PRB Coefficient Origins
γ, c_θ, and K_θ are drawn from the fixed-pinned vertical-load PRB family.
My PRB coefficients are chosen to match the selected coupler path.
These values differ from the classical Howell-Midha stiffness coefficient.

## Slide 9
FEA Methodology
Abaqus model mirrors the PRB concept with rigid members and a torsional spring.
Characteristic pivot is the crank-coupler connection.
Coupler path uses a characteristic radius of 0.85L_c.

## Slide 10
FEA Implementation Notes
FEA assumes rigid links and torsional spring behavior at the pivot.
Slider displacement is extracted along the grounded path.
Torque result is included with caution due to numerical validation limits.

## Slide 11
Results: Torque Comparison
Compare My PRB and Howell-Midha torque predictions.
Available Abaqus torque result shown as reference.
Different stiffness assumptions drive torque divergence.

## Slide 12
Results: Displacement Comparison
Slider displacement is the primary kinematic metric.
Both PRB models show similar trends but differ in path assumptions.
FEA displacement provides a useful numerical check.

## Slide 13
Model Discrepancies Explained
Howell-Midha uses classical PRB path with standard stiffness coefficients.
My PRB uses a tailored tip path and coefficient set.
Small changes in path and spring definition affect torque and displacement.

## Slide 14
Interactive App Description
MATLAB-based GUI allows parameter modification.
Displays analytical PRB predictions and FEA-based results.
Visualizes discrepancy between models.

## Slide 15
Conclusions and Future Work
The PRB models capture general mechanism behavior.
FEA validates the selected PRB geometry, especially displacement.
Future work: improve the analytical model and increase numerical robustness.

## Slide 16
References
Howell and Midha, ASME J. Mech. Design, 1995.
Professor H. Su lecture slides, OSU Advanced Kinematics.
Project-specific PRB and FEA methodology.